# Version history
Version 2 Last saved 17. Dec. 2023 18:41 Wim Beaumont
Author W. Beaumont
## document status
Internal use but can be shared
for discussion
none private or sensitive information
# introduction

The Julabo FP51-SL can be controlled by a computer via the RS232 communication protocol.
The connector on the device is a sub D 9 female connector . BUT this is NOT compatible with the standard CTE connector ( a 1 : 1 female subD 9 to male subD 9 connector can be destructive !!)
A special cable has to be made .
Info about the cable that links to this document :
length ~ 40cm
cable Alpha wire 1176L
un-screened, 6 cores , 22AWG
hoods MHCCOV-9SC-LG (or CCOV-9SC-LG , 2360-0102-11 ,Farnell order code 3938013)

Function PC	To PC	To / chiller	Function chiller	Wire color
	Female sub D 9	Male sub D 9
nc	1	1	nc	Not connected
RX	2	3	TX	red
TX	3	2	RX	green
nc	4	4	nc
GND	5	5	GND
nc	6	6	nc
RTS	7	8	CTS	blue
CTS	8	7	RTS	orange
nc	9	9	nc
nc			nc	white

# additional info

Figure 1: information about the sub D 9 connector on the Julabo FP51-SL